## Slide 1: Selected Design Topics

## Slide 2: Integrated Circuits
Integrated circuit (informally, a “chip”) is a semiconductor crystal (most often silicon) containing the electronic components for the digital gates and storage elements which are interconnected on the chip.
Terminology - Levels of chip integration
  SSI (small-scale integrated) - fewer than 10 gates
  MSI (medium-scale integrated) - 10 to 100 gates
  LSI (large-scale integrated) - 100 to thousands of gates
  VLSI (very large-scale integrated) - thousands to 100s of millions of gates

## Slide 3: Technology Parameters
Fan-in – the number of inputs available on a gate
Fan-out – the number of standard loads driven by a gate output
Logic Levels – the signal value ranges for 1 and 0 on the inputs and 1 and 0 on the outputs
Noise Margin – the maximum external noise voltage superimposed on a normal input value that will not cause an undesirable change in the circuit output
Cost for a gate - a measure of the contribution by the gate to the cost of the integrated circuit
Propagation Delay – The time required for a change in the value of a signal to propagate from an input to an output
Power Dissipation – the amount of power drawn from the power supply and consumed by the gate

## Slide 4: Fan-out
Fan-out can be defined in terms of a standard load
Example: 1 standard load equals the load contributed by the input of 1 inverter.
Transition time -the time required for the gate output to change from H to L, or from L to H
The maximum fan-out that can be driven by a gate is the number of standard loads the gate can drive without exceeding its specified maximum transition time

## Slide 5: Cost
In an integrated circuit:
  The cost of a gate is proportional to the chip area occupied by the gate
  The gate area is roughly proportional to the number and size of the transistors and the amount of wiring connecting them
  Ignoring the wiring area, the gate area is roughly proportional to the gate input count
  So gate input count is a rough measure of gate cost
If the actual chip layout area occupied by the gate is known, it is a far more accurate measure

## Slide 6: Propagation Delay
Propagation delay is the time for a change on an input of a gate to propagate to the output.
High-to-low (tPHL) and low-to-high (tPLH) output signal changes may have different propagation delays.
=

## Slide 7: Circuit Delay
A
0.4
0.5
0.4
S
B
Y
0.2
2-input multiplexer
  Y = A for S = 1
  Y = B for S = 0

## Slide 8: Fan-out and Delay
The fan-out loading a gate’s output affects the gate’s propagation delay
Example:
  One realistic equation for tpd for a NAND gate with 4 inputs is:
    tpd = 0.07 + 0.021 SL ns
  SL is the number of standard loads the gate is driving, i. e., its fan-out in standard loads
  For SL = 4.5, tpd = 0.165 ns
If this effect is considered, the delay of a gate in a circuit takes on different values depending on the circuit load on its output.

## Slide 9: Flip-Flop Timing Parameters
ts - setup time
th - hold time
tw – clock pulse width
tpx – propa-gation delay
  tPHL - High-to-Low
  tPLH - Low-to-High
  tpd - max (tPHL, tPLH)
t
s
t
h
t
p-,min
t
p-,max
t
w
C
D
Q
(b) Edge-triggered (negative edge)
t
h
t
s
t
p-,min
t
p-,max
t
w
C
S
/
R
Q
(a) Pulse-triggered (positive pulse)

## Slide 10: Circuit and System Level Timing
Consider a system of flip-flops connected by logic
If the clock period is too short, some data changes will not propagate through the circuit to flip-flop inputs before the setup time interval begins
C
D
Q
Q'
C
D
Q
Q'
C
D
Q
Q'
C
D
Q
Q'
C
D
Q
Q'
C
D
Q
Q'
C
D
Q
Q'
C
D
Q
Q'
C
D
Q
Q'
C
D
Q
Q'
CLOCK
CLOCK