## Slide 1: Memory Basics

## Slide 2: Memory Definitions
Memory A collection of storage cells together with the necessary circuits to transfer information to and from them.
  Organized as an indexed array of words.
    Word - a typical unit of access for the memory.
  Value of the index for each word is the memory address.
Memory Organization ─ the basic architectural structure of a memory in terms of how data is accessed.
Random Access Memory (RAM) ─ a memory organized such that data can be transferred to or from any cell (or collection of cells) in a time that is not dependent upon the particular cell selected.

## Slide 3: Basic Memory Operations
Data
  data written to, or read from, memory
Address
  specifies the memory location to operate on
An operation
  control information which specifies the type of operation to be performed.
  Typical operations are READ and WRITE.
CS
Read/Write

## Slide 4: Basic Memory Operations (continued)
Write Memory ─ an operation that writes a data value to memory:
  Place a valid address on the address lines and valid data on the data lines.
  Toggle the memory write control line

## Slide 5: Basic Memory Operations (continued)
Read Memory ─ an operation that reads a data value stored in memory:
  Place a valid address on the address lines.
  Wait for the read data to become stable.

## Slide 6: RAM Integrated Circuits
Types of random access memory
  Static – information stored in latches
  Dynamic – information stored as electrical charges on capacitors
    Charge “leaks” off
    Periodic refresh of charge required
Dependence on Power Supply
  Volatile – loses stored information when power turned off
  Non-volatile – retains information when power turned off

## Slide 7: Static RAM Cell
Array of storage cells used to implement static RAM
Storage Cell
  SR Latch
  Select input for control

## Slide 8: Static RAM Bit Slice
2n 1-bit words
  Multiple RAM cells
  Control Lines:
    Word select
    Bit Select
  Data Lines:
    Data in
    Data out

## Slide 9: 2n-Word  1-Bit RAM IC
Read/
To build a RAM IC from a RAM slice, we need:
  Decoder decodes the n address lines to 2n word select lines
  A 3-state buffer
  on the data output permits RAM ICs to be combined into a RAM with c  2n words
Word select
Read/Write
logic
Data in
Data out
Write
Bit
select
(b) Block diagram
RAM cell
RAM cel
l
RAM cell
Data input
Chip select
Read/Write
Data
output
A
3
A
2
A
1
A
0
2
3
2
2
2
1
2
0
4-to-16
Decoder
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
A
3
A
2
A
1
A
0
Data
input
Data
output
(a) Symbol
Read/
Write
Memory
enable
16 x
1
RAM
Memory arrays can be very large!!!
  Large decoders
  Large fanouts for the bit lines

## Slide 10: Cell Arrays and Coincident Selection
Data input
Read/Write
X
X
X
A
1
A
0
RAM cell
0
RAM cell
4
RAM cell
8
RAM cell
12
Read/Write
logic
Data in
Data out
Read/
Write
Bit
select
RAM cell
1
RAM cell
5
RAM cell
9
RAM cell
13
Read/Write
logic
Data in
Data out
Read/
Write
Bit
select
RAM cell
2
RAM cell
6
RAM cell
10
RAM cell
14
Read/Write
logic
Data in
Data out
Read/
Write
Bit
select
RAM cell
3
RAM cell
7
RAM cell
11
RAM cell
15
Read/Write
logic
Data in
Data out
Read/
Write
Bit
select
Column
decoder
2-to-4 Decoder
with enable
2
1
2
0
0
1
Column select
2
Enable
3
Chip select
Data
output
Row
select
Row decoder
A
2
A
3
X
2-to-4
Decoder
2
0
2
1
1
2
3
0
The decoder size and fanouts can be reduced by approximately by using a coincident selection in a 2-dimensional array
16x1 RAM using 4x4 RAM Cell Array

## Slide 11: Larger Memories
256Kx8 RAM ?
64K words of 8 bits each

## Slide 12: Wider Memories
64Kx16 RAM?
64K words of 8 bits each

## Slide 13: Dynamic RAM (DRAM)
Basic Principle: Storage of information on capacitors.
Charge and discharge of capacitor to change stored value
Use of transistor as “switch” to:
  Store charge
  Charge or discharge
SRAM cell contains 6 transistors!
3 times cell complexity!
Size??

## Slide 14: Dynamic RAM - Bit Slice
Sense amplifier is used to change the small voltage change on C into H or L
In the electronics, B, C, and the sense amplifier output are connected to make destructive read into non-destructive read

## Slide 15: Dynamic RAM - Block Diagram

## Slide 16: Dynamic RAM Write Timing

## Slide 17: Dynamic RAM Read Timing

## Slide 18: DRAM Types