## Slide 1: Computer Design Basics

## Slide 2: Introduction
Computer Specification
  Instruction Set Architecture (ISA) - the specification of a computer's appearance to a programmer at its lowest level
  Computer Architecture - a high-level description of the hardware implementing the computer derived from the ISA
    The architecture usually includes additional specifications such as speed, cost, and reliability.

## Slide 3: Simple Computer Architecture
Simple computer architecture decomposed into:
  Datapath for performing operations
  Control unit for controlling datapath operations
A datapath is specified by:
  A set of registers
  The microoperations performed on the data stored in the registers
  A control interface

## Slide 4: Datapaths
The set of registers
    A set of registers with common access resources called a register file
Microoperation implementation
    Buses - shared transfer paths
    Arithmetic-Logic Unit (ALU) - shared resource for implementing arithmetic and logic microoperations
    Shifter - shared resource for implementing shift microoperations

## Slide 5: Datapath Example
Four parallel-load registers
Two mux-based register selectors
Register destination decoder
Mux B for external constant input
Buses A and B with external address and data outputs
ALU and Shifter with Mux F for output select
Mux D for external data input
Logic for generating status bits V, C, N, Z

## Slide 6: Datapath Example: Performing a Microoperation
Microoperation: R0 ← R1 + R2
Apply 01 to A select to place contents of R1 onto Bus A
Apply 10 to B select to place contents of R2 onto B data and apply 0 to MB select to place B data on Bus B
Apply 0010 to G select to perform addition G = Bus A + Bus B
Apply 0 to MF select and 0 to MD select to place the value of G onto BUS D
Apply 00 to Destination select to enable the Load input to R0
Apply 1 to Load Enable to force the Load input to R0 to 1 so that R0 is loaded on the clock pulse (not shown)
The overall microoperation requires 1 clock cycle

## Slide 7: Arithmetic Logic Unit (ALU)
Decompose the ALU into:
  An arithmetic circuit
  A logic circuit
  A selector to pick between the two circuits

## Slide 8: Arithmetic Circuit Design

## Slide 9: Example: 4-bit Arithmetic Circuit

## Slide 10: Logic Circuit

## Slide 11: Arithmetic Logic Unit (ALU)
Gi

## Slide 12: The Shifter
4-Bit Basic Shifter

## Slide 13: Barrel Shifter

## Slide 14: Datapath Representation
Boolean Equations:
MFS = F3 F2
GSi = Fi
HSi = Fi

## Slide 15: Datapath With Function Unit Select Codes
G
Select,
H
Select,
and
MF
in T
of
FS
Codes

## Slide 16: The Control Word
The datapath has many control inputs
The signals driving these inputs can be defined and organized into a control word
To execute a microinstruction, we apply control word values for a clock cycle.
  For most microoperations, the positive edge of the clock cycle is needed to perform the register load

## Slide 17: Control Word
10
8
14
0
13
11
Bus D
Constant in
n
n
MUX B
1
0
D data
Write
D address
A address
B address
A data
B data
8
x
n
Register file
A
B
Function
unit
n
n
n
MUX D
0
1
n
n
Data in
Bus A
Bus B
R
W
12
AA
15
D
A
n
BA
9
Address out
Data out
V
C
N
Z
7
MD
1
MB
6
4
FS
5
3
2

## Slide 19: Datapath Simulation
10
8
14
0
13
11
Bus D
Constant in
n
n
MUX B
1
0
D data
Write
D address
A address
B address
A data
B data
8
x
n
Register file
A
B
Function
unit
n
n
n
MUX D
0
1
n
n
Data in
Bus A
Bus B
R
W
12
AA
15
D
A
n
BA
9
Address out
Data out
V
C
N
Z
7
MD
1
MB
6
4
FS
5
3
2