## Slide 1: A Simple Computer Architecture

## Slide 2: Breakdown of a Computing Problem
Instruction Set Architecture (ISA)
Problem
Algorithms
Programming in
High-Level Language
Compiler/Assembler/
Linker
System Level
Human Level
System architecture
Target Machine
(one implementation)
Micro-architecture
Functional units/
Data Path
Gates Level
Design
Transistors
Manufacturing
RTL Level
Logic Level
Circuit Level
Silicon Level

## Slide 3
10
8
14
0
13
11
Bus D
Constant in
n
n
MUX B
1
0
D data
Write
D address
A address
B address
A data
B data
8
x
n
Register file
A
B
Function
unit
n
n
n
MUX D
0
1
n
n
Data in
Bus A
Bus B
R
W
12
AA
15
D
A
n
BA
9
Address out
Data out
V
C
N
Z
7
MD
1
MB
6
4
FS
5
3
2
DATAPATH
Control Word
How to program & control ?

## Slide 4: ISA design principles
High Level Language
ISA
Compiler
…
lw r2, mem[r7]
add r3, r4, r2
st r3, mem[r8]
main() {
int i,b,c,a[10];
for (i=0; i<10; i++)…
a[2] = b + c*i;
}
Assembler
Binary code

## Slide 5: General Purpose Computer
Central Processing Unit
(CPU)
Memory
Data
Data &
Instruction
0101 1001 1010 1001 1000
0100 1000 1110 1111 0011
0010 1011 1000 …… ……
A stored-program computer called EDVAC proposed in 1944 while developing ENIAC, first general purpose computer
Contributors:
Presper Eckert
John Mauchly
John von Neumann
Von Neumann Machine

## Slide 6: Basic Operation
1000 1100 1110 0010 0000 0000 0000 0000
Instruction fetch from memory
Control Unit
Datapath Unit
Data written back to memory
It’s called Harvard Architecture (Mark-III/IV) if instruction and data memory are separated
MICROPROCESSOR

## Slide 7: Program Counter
How a sequence of instructions are fetched and executed by a computer?
Program Counter (PC)
  A special register
  Provide the logical ordering of a program
  Point to the address of the instruction to be executed
main:
la $8, array
lb $9, ($8)
lb $10, 1($8)
add $11, $9, $10
sb $11, ($8)
addiu $8, $8, 4
lh $9, ($8)
lhu $10, 2($8)
add $11, $9, $10
sh $11, ($8)
addiu $8, $8, 4
lw $9, ($8)
lw $10, 4($8)
sub $11, $9, $10
sw $11, ($8)
PC

## Slide 8: Instruction Set Architecture (ISA) for Simple Computer (SC)
A programmable system uses a sequence of instructions to control its operation
An typical instruction specifies:
  Operation to be performed
  Operands to use, and
  Where to place the result, or
  Which instruction to execute next
Instructions are stored in RAM or ROM as a program
The addresses for instructions in a computer are provided by a program counter (PC) that can
  Count up
  Load a new address based on an instruction and, optionally, status information

## Slide 9: Instruction Set Architecture (ISA)
The PC and associated control logic are part of the Control Unit
Executing an instruction - activating the necessary sequence of operations specified by the instruction
Execution is controlled by the control unit and performed:
  In the datapath
  In the control unit
  In external hardware such as memory or input/output

## Slide 10: ISA: Storage Resources
The storage resources are "visible" to the programmer at the lowest software level (typically, machine or assembly language)
Separate instruction and data memories imply "Harvard architecture"

## Slide 11: ISA: Instruction Format
A instruction consists of a bit vector
The fields of an instruction are subvectors representing specific functions and having specific binary codes defined
The format of an instruction defines the subvectors and their function

## Slide 12: ISA: Instruction Format (continued)
This format supports instructions represented by:
  R1 ← R2 + R3
  R1 ← sl R2
There are three 3-bit register fields:
  DR - specifies destination register (R1 in the examples)
  SA - specifies the A source register (R2 in the first example)
  SB - specifies the B source register (R3 in the first example and R2 in the second example)
(a) Register
Opcode
Destination
register (DR)
Source reg-
ister A (SA)
Source reg-
ister B (SB)
15
9
8
6
5
3
2
0

## Slide 13: ISA: Instruction Format (continued)
(b) Immediate
Opcode
Destination
register (DR)
Source reg-
ister A (SA)
15
9
8
6
5
3
2
0
Operand (OP)
This format supports instructions described by:
  R1 ← R2 + 3
The B Source Register field is replaced by an Operand field OP which specifies a constant.
The Operand:
  3-bit constant
  Values from 0 to 7
The constant:
  Zero-fill (on the left of) the Operand to form 16-bit constant
  16-bit representation for values 0 through 7

## Slide 14: ISA: Instruction Format (continued)
This instruction supports changes in the sequence of instruction execution by adding an extended, 6-bit, signed 2s-complement address offset to the PC value
The 6-bit Address (AD) field replaces the DR and SB fields
  Example: Suppose that a jump is specified by the Opcode and the PC contains 45 (0…0101101) and Address contains – 12 (110100). Then the new PC value will be: 0…0101101 + (1…110100) = 0…0100001 (45 + (– 12) = 33)
The SA field is retained to permit jumps and branches on N or Z based on the contents of Source register A
(c) Jump and Branch
Opcode
Source reg-
ister A (SA)
15
9
8
6
5
3
2
0
Address (AD)
(Right)
Address (AD)
(Left)

## Slide 15: ISA: Instruction Specifications

## Slide 16: ISA:Example Instructions

## Slide 17: Single-Cycle Hardwired Control
Based on the ISA defined, design a computer architecture to support the ISA
The architecture is to fetch and execute each instruction in a single clock cycle
  PL – load enable for the PC
  JB – Jump/Branch select:
  If JB = 1, Jump, else Branch
  BC – Branch Condition select: If BC = 1, branch for N = 1, else branch for Z = 1.
The PC is controlled by Branch Control logic

## Slide 18: PC Function
PC function is based on instruction specifications involving jumps and branches
In addition to the above register transfers, the PC must also implement: PC ← PC + 1
The first two transfers above require addition to the PC of: Address Offset = Extended IR(8:6) || IR(2:0)
The third transfer requires that the PC be loaded with: Jump Address = Bus A = R[SA]
The counting function of the PC requires addition to the PC of 1
Branch
on
Zero
BRZ
if (R[
S
A] =
0) PC
←
PC
+ s
e
A
D
Branch
on
Negative
BRN
if (R[
S
A] <
0) PC
PC
+ s
e
A
D
J
u
mp
JMP
P
C
R[SA
]
←
←

## Slide 19: Instruction Decoder
The combinational instruction decoder converts the instruction into the signals necessary to control all parts of the computer during the single cycle execution
The input is the 16-bit Instruction
The outputs are control signals:
  Register file addresses DA, AA, and BA,
  Function Unit Select FS
  Multiplexer Select Controls MB and MD,
  Register file and Data Memory Write Controls RW and MW, and
  PC Controls PL, JB, and BC
The register file outputs are simply pass-through signals: DA = DR, AA = SA, and BA = SB .

## Slide 21: Example Instruction Execution

## Slide 22: Decoding for ADI
19
–
17
DA
16
–
14
AA
13
–
11
BA
10
MB
9
–
6
FS
5
MD
4
RW
3
MW
2
PL
1
JB
0
BC
Instruction
Opcode
DR
SA
SB
Control word
15
14
13
12
11
10
9
8
–
6
5
–
3
2
–
0
1 0 0 0 0 1 0
1
1
0 0 1 0
0
0
0
0
0

## Slide 23
Bus A
Bus B
Address out
Data out
MW
Data in
MUX B
1
0
MUX D
0
1
DATAPATH
RW
DA
AA
Constant
in
BA
MB
FS
V
C
N
Z
Function
unit
A
B
F
MD
Bus D
IR(2:0)
Data in
Address
Data
memory
Data out
Register
file
D
A
B
Instruction
memory
Address
Instruction
Zero fill
D
A
B
A
A
A
F
S
M
D
R
W
M
W
M
B
Instruction decoder
J
B
Extend
L
P
B
C
Branch
Control
V
C
N
Z
J
B
L
P
B
C
IR(8:6) || IR(2:0)
PC
CONTROL
Control Inputs and Paths for ADI
1
1
0 0 1 0
0
0
0
0
0
0 0 1 0
1
0
1
0
0
0
0
+
No Write
Increment PC

## Slide 24: Decoding for LD
19
–
17
DA
16
–
14
AA
13
–
11
BA
10
MB
9
–
6
FS
5
MD
4
RW
3
MW
2
PL
1
JB
0
BC
Instruction
Opcode
DR
SA
SB
Control word
15
14
13
12
11
10
9
8
–
6
5
–
3
2
–
0
0 0 1 0 0 0 0
0
1
0 0 0 0
1
0
0
1
0

## Slide 25
Bus A
Bus B
Address out
Data out
MW
Data in
MUX B
1
0
MUX D
0
1
DATAPATH
RW
DA
AA
Constant
in
BA
MB
FS
V
C
N
Z
Function
unit
A
B
F
MD
Bus D
IR(2:0)
Data in
Address
Data
memory
Data out
Register
file
D
A
B
Instruction
memory
Address
Instruction
Zero fill
D
A
B
A
A
A
F
S
M
D
R
W
M
W
M
B
Instruction decoder
J
B
Extend
L
P
B
C
Branch
Control
V
C
N
Z
J
B
L
P
B
C
IR(8:6) || IR(2:0)
PC
CONTROL
Control Inputs and Paths for LD
0
1
0 0 0 0
1
0
0
1
0
0 0 0 0
0
1
1
0
0
1
0
No Write
Increment PC

## Slide 26: Decoding for BRZ
19
–
17
DA
16
–
14
AA
13
–
11
BA
10
MB
9
–
6
FS
5
MD
4
RW
3
MW
2
PL
1
JB
0
BC
Instruction
Opcode
DR
SA
SB
Control word
15
14
13
12
11
10
9
8
–
6
5
–
3
2
–
0
1 1 0 0 0 0 0
1
0
0 0 0 0
0
1
0
0
0

## Slide 27
Bus A
Bus B
Address out
Data out
MW
Data in
MUX B
1
0
MUX D
0
1
DATAPATH
RW
DA
AA
Constant
in
BA
MB
FS
V
C
N
Z
Function
unit
A
B
F
MD
Bus D
IR(2:0)
Data in
Address
Data
memory
Data out
Register
file
D
A
B
Instruction
memory
Address
Instruction
Zero fill
D
A
B
A
A
A
F
S
M
D
R
W
M
W
M
B
Instruction decoder
J
B
Extend
L
P
B
C
Branch
Control
V
C
N
Z
J
B
L
P
B
C
IR(8:6) || IR(2:0)
PC
CONTROL
Control Inputs and Paths for BRZ
1
0
0 0 0 0
0
1
0
0
0
0 0 0 0
1
0
0
0
1
0
0
No Write
Branch on
Z
No Write

## Slide 28: Single-Cycle Computer Issues
Shortcoming of Single Cycle Design
  Complexity of instructions executable in a single cycle is limited
  Accessing both an instruction and data from a simple single memory impossible
  A long worst case delay path limits clock frequency and the rate of performing instructions