## Slide 1: A Simple Computer Architecture

## Slide 2: Instruction Set Architecture (ISA) for Simple Computer (SC)
A programmable system uses a sequence of instructions to control its operation
An typical instruction specifies:
  Operation to be performed
  Operands to use, and
  Where to place the result, or
  Which instruction to execute next
Instructions are stored in RAM or ROM as a program
The addresses for instructions in a computer are provided by a program counter (PC) that can
  Count up
  Load a new address based on an instruction and, optionally, status information

## Slide 3: Instruction Set Architecture (ISA)
The PC and associated control logic are part of the Control Unit
Executing an instruction - activating the necessary sequence of operations specified by the instruction
Execution is controlled by the control unit and performed:
  In the datapath
  In the control unit
  In external hardware such as memory or input/output

## Slide 4: ISA: Storage Resources
The storage resources are "visible" to the programmer at the lowest software level (typically, machine or assembly language)
Separate instruction and data memories imply "Harvard architecture"

## Slide 5: ISA: Instruction Format
A instruction consists of a bit vector
The fields of an instruction are subvectors representing specific functions and having specific binary codes defined
The format of an instruction defines the subvectors and their function
  R1 ← R2 + R3
  R1 ← sl R2
  R1 ← R2 + 3
Change the sequence of instruction execution by adding an extended, 6-bit, signed 2s-complement address offset to the PC value

## Slide 6: ISA: Instruction Specifications

## Slide 7: ISA:Example Instructions and Data in Memory

## Slide 8: Single-Cycle Hardwired Control
Based on the ISA defined, design a computer architecture to support the ISA
The architecture is to fetch and execute each instruction in a single clock cycle
  PL – load enable for the PC
  JB – Jump/Branch select:
  If JB = 1, Jump, else Branch
  BC – Branch Condition select: If BC = 1, branch for N = 1, else branch for Z = 1.

## Slide 9: Instruction Decoder
The combinational instruction decoder converts the instruction into the signals necessary to control all parts of the computer during the single cycle execution
The input is the 16-bit Instruction
The outputs are control signals:
  Register file addresses DA, AA, and BA,
  Function Unit Select FS
  Multiplexer Select Controls MB and MD,
  Register file and Data Memory Write Controls RW and MW, and
  PC Controls PL, JB, and BC
The register file outputs are simply pass-through signals: DA = DR, AA = SA, and BA = SB .

## Slide 11: Example Instruction Execution

## Slide 12: Decoding for ADI
19
–
17
DA
16
–
14
AA
13
–
11
BA
10
MB
9
–
6
FS
5
MD
4
RW
3
MW
2
PL
1
JB
0
BC
Instruction
Opcode
DR
SA
SB
Control word
15
14
13
12
11
10
9
8
–
6
5
–
3
2
–
0
1 0 0 0 0 1 0
1
1
0 0 1 0
0
0
0
0
0

## Slide 13
Bus A
Bus B
Address out
Data out
MW
Data in
MUX B
1
0
MUX D
0
1
DATAPATH
RW
DA
AA
Constant
in
BA
MB
FS
V
C
N
Z
Function
unit
A
B
F
MD
Bus D
IR(2:0)
Data in
Address
Data
memory
Data out
Register
file
D
A
B
Instruction
memory
Address
Instruction
Zero fill
D
A
B
A
A
A
F
S
M
D
R
W
M
W
M
B
Instruction decoder
J
B
Extend
L
P
B
C
Branch
Control
V
C
N
Z
J
B
L
P
B
C
IR(8:6) || IR(2:0)
PC
CONTROL
Control Inputs and Paths for ADI
1
1
0 0 1 0
0
0
0
0
0
0 0 1 0
1
0
1
0
0
0
0
+
No Write
Increment PC

## Slide 14: Decoding for LD
19
–
17
DA
16
–
14
AA
13
–
11
BA
10
MB
9
–
6
FS
5
MD
4
RW
3
MW
2
PL
1
JB
0
BC
Instruction
Opcode
DR
SA
SB
Control word
15
14
13
12
11
10
9
8
–
6
5
–
3
2
–
0
0 0 1 0 0 0 0
0
1
0 0 0 0
1
0
0
1
0

## Slide 15
Bus A
Bus B
Address out
Data out
MW
Data in
MUX B
1
0
MUX D
0
1
DATAPATH
RW
DA
AA
Constant
in
BA
MB
FS
V
C
N
Z
Function
unit
A
B
F
MD
Bus D
IR(2:0)
Data in
Address
Data
memory
Data out
Register
file
D
A
B
Instruction
memory
Address
Instruction
Zero fill
D
A
B
A
A
A
F
S
M
D
R
W
M
W
M
B
Instruction decoder
J
B
Extend
L
P
B
C
Branch
Control
V
C
N
Z
J
B
L
P
B
C
IR(8:6) || IR(2:0)
PC
CONTROL
Control Inputs and Paths for LD
0
1
0 0 0 0
1
0
0
1
0
0 0 0 0
0
1
1
0
0
1
0
No Write
Increment PC

## Slide 16: Decoding for BRZ
19
–
17
DA
16
–
14
AA
13
–
11
BA
10
MB
9
–
6
FS
5
MD
4
RW
3
MW
2
PL
1
JB
0
BC
Instruction
Opcode
DR
SA
SB
Control word
15
14
13
12
11
10
9
8
–
6
5
–
3
2
–
0
1 1 0 0 0 0 0
1
0
0 0 0 0
0
1
0
0
0

## Slide 17
Bus A
Bus B
Address out
Data out
MW
Data in
MUX B
1
0
MUX D
0
1
DATAPATH
RW
DA
AA
Constant
in
BA
MB
FS
V
C
N
Z
Function
unit
A
B
F
MD
Bus D
IR(2:0)
Data in
Address
Data
memory
Data out
Register
file
D
A
B
Instruction
memory
Address
Instruction
Zero fill
D
A
B
A
A
A
F
S
M
D
R
W
M
W
M
B
Instruction decoder
J
B
Extend
L
P
B
C
Branch
Control
V
C
N
Z
J
B
L
P
B
C
IR(8:6) || IR(2:0)
PC
CONTROL
Control Inputs and Paths for BRZ
1
0
0 0 0 0
0
1
0
0
0
0 0 0 0
1
0
0
0
1
0
0
No Write
Branch on
Z
No Write

## Slide 18: Single-Cycle Computer Issues
Shortcoming of Single Cycle Design
  Complexity of instructions executable in a single cycle is limited
  Accessing both an instruction and data from a simple single memory impossible
  A long worst case delay path limits clock frequency and the rate of performing instructions