## Slide 1: Hardware Description Languages

## Slide 2: Introduction
A drawing of a circuit, or schematic, contains graphical information about a design
  Inverter is above the OR gate, AND gate is to the right, etc.
Such graphical information may not be useful for large designs
Can use textual language instead
si
g
t
o
c
o
n
t
r
a
tap
a
D
oorOpener
c
h
p
f

## Slide 3: Computer-Readable Textual Language for Describing Hardware Circuits: HDLs
Hardware description language (HDL)
  Intended to describe circuits textually, for a computer to read
  Evolved starting in the 1970s and 1980s
Popular languages today include:
  VHDL –Defined in 1980s by U.S. military; Ada-like language
  Verilog –Defined in 1980s by a company; C-like language
  SystemC –Defined in 2000s by several companies; consists of libraries in C++

## Slide 4: Describing Structure in VHDL

## Slide 5: Describing Combinational Behavior in VHDL
Describing an OR gate's behavior
  Entity defines input/output ports
  Architecture
    Process – Describes behavior
      Behavior assigns a new value to output port F, computed using built-in operator "or"
library
ieee;
use
ieee.std_logic_1164.all;
entity
OR2
is
port
(x, y:
in
std_logic;
F:
out
std_logic
);
end
OR2;
architecture
behavior
of
OR2
is
begin
process
(x, y)
begin
F <= x
or
y;
end process
;
end
behavior;
Describing a custom function's behavior
  Desired function: f = c'*(h+p)
architecture
beh
of
DoorOpener
is
begin
process
(c, h, p)
begin
f <=
not
(c)
and
(h
or
p);
end process
;
end
beh;

## Slide 6: Testbenches
Testbench
  Assigns values to a system's inputs, check that system outputs correct values
  A key use of HDLs is to simulate system to ensure design is correct
SystemToTest
Testbench
Set input values, check output values

## Slide 7: Testbench in VHDL
Entity
  No inputs or outputs
Architecture
  Declares component to test, declares signals
  Instantiates component, connects to signals
  Process writes input signals, checks output signal
    Waits a small amount of time after writing input signals
    Checks for correct output value using "assert" statement
SystemToTest
Testbench
Set input values, check output values
process
DoorOpener1

## Slide 8: Describing a Full-Adder in VHDL
Entity
  Declares inputs/outputs
Architecture
  Described behaviorally (could have been described structurally)
  Process sensitive to inputs
  Computes expressions, sets outputs
s = a xor b xor ci
co = bc + ac + ab
c
o
ci
b
a
s
Full adder

## Slide 9: Describing a Carry-Ripple Adder in VHDL
Entity
  Declares inputs/outputs
  Uses std_logic_vector for 4-bit inputs/outputs
Architecture
  Described structurally by composing four full-adders (could have been described behaviorally instead)
  Declares full-adder component, instantiates four full-adders, connects
    Note use of three internal signals for connecting carry-out of one stage to carry-in of next stage
a3
c
o
s
F
A
c
o
b3
a2
b2
s3
s2
s1
ci
b
a
c
o
s
F
A
ci
b
a
a1
b1
c
o
s
F
A
ci
b
a
s0
a0
b0
ci
c
o
s
F
A
ci
b
a
co1
co2
co3

## Slide 10: Describing a 4-bit Register in VHDL
Entity
  4 data inputs, 4 data outputs, and a clock input
  Use std_logic_vector for 4-bit data
    I: in std_logic_vector(3 downto 0)
    I <= "1000" would assign I(3)=1, I(2)=0, I(1)=0, I(0)=0
Architecture
  Process sensitive to clock input
    First statement detects if change on clock was a rising edge
    If clock change was rising edge, sets output Q to input I
    Ports are signals, and signals store values – thus, output retains new value until set to another value

## Slide 11: Describing an Up-Counter in VHDL
Described structurally (could have been described behaviorally)
Includes process that updates output port C whenever internal signal tempC changes
  Need tempC signal because can't read C due to C being an output port
ld
4-bit register
C
t
c
4
4
4
4
c
n
t
4-bit up-counter
+1
tempC

## Slide 12: Describing an Oscillator in VHDL
Entity
  Defines clock output
Architecture
  Process
    Has no sensitivity list, so executes non-stop as infinite loop
    Sets clock to 0, waits 10 ns, sets clock to 1, waits 10 ns, repeats

## Slide 13: Describing a Controller in VHDL
Inputs: b; Outputs: x
On2
On1
On3
Off
x=1
x=1
x=1
x=0
b
’
b
FSM behavior captured using architecture with 2 processes
  First process models state register
    Asynchronous reset sets state to "S_Off"
    Rising clock edge sets currentstate to nextstate
  Second process models combinational logic
    Sensitive to currentstate and FSM inputs
    Sets FSM outputs based on currentstate
    Sets nextstate based on currentstate and present FSM input values
  Note declaration of new type, statetype
Combinational
logic
State register
s1
s0
n1
n0
x
b
clk
FSM
inputs
FSM
outputs

## Slide 14: Summary
Hardware Description Languages (HDLs) are widely used in modern digital design
  Textual rather than graphical language sufficient for many purposes
  HDLs are computer-readable
  Great for simulation
VHDL, Verilog, and SystemC are popular
Introduced languages mainly through examples
Numerous HDL books exist to teach each language in more detail