## Slide 1: Chapter 4: Peripheral programming in C
Stellaris® Cortex-M3 - Microcontroller Family
Texas Instruments
Texas Instruments - University Program
Heilbronn University, Campus Künzelsau
Prof. Dr.-Ing. Ralf Gessler Rev. 1.0

## Slide 2: Content
Chapter 4: Peripheral Programming in C 4.1 General Purpose IO (GPIO) 4.2 Interrupt functions 4.3 Timers: General purpose and PWM 4.4 Analogue: ADC 4.5 Serial interfaces: UART
Topics: timer, PWM, interrupts, GPIO, NVIC, EKS-LM3S1968, LED, OLED, StellarisWare®, API, C language

## Slide 3: Learning Objectives
This chapter gives practical experience of the Stellaris® timers and timer-interrupts.
The StellarisWare® API is applied to control the timer interrupts
Application “Blinky with timer” triggers the on-board LED
Structure and questions:
  What does the General-Purpose Timer Module look like?
  What are the features of the General-Purpose Timer?
  How can I apply StellarisWare® to running the general purpose timers?

## Slide 4: General view
Timer
  Principle
    A simple counter
    Runs to pre-defined value (e.g. to a maximum)
    Triggers an interrupt
    Interrupt frequency depends on the pre-defined counter value or the register clocking
  Application (example)
    Time base
Pulse-Width-Modulation (PWM)
  Principle
    Based on a timer
    Control the electrical energy by modulating the pulse-width
  Application (example)
    Motor control

## Slide 5: Overview: Stellaris®
Explanations
based on
Stellaris®
LM3S1968
80 MHz

## Slide 6: Main Features
Four General-Purpose Timer Modules (GPTM)
  Referred to as Timer0, Timer1, Timer 2, and Timer 3
each GPTM provides two 16-bit timers/counters
  Referred to as TimerA and TimerB.
each GPTM can be configured to operate independently:
  As a single 32-bit timer
  As one 32-bit Real-Time Clock (RTC) to event capture
  For Pulse Width Modulation (PWM)
  To trigger analog-to-digital conversions
32-bit Timer modes
  Programmable one-shot timer
  Programmable periodic timer
  Real-Time Clock when using an external 32.768-KHz clock as the input
  User-enabled stalling when the controller asserts CPU Halt flag during debug
  ADC event trigger

## Slide 7: Main Features
16-bit Timer modes
  General-purpose timer function with an 8-bit pre-scaler (for one-shot and periodic modes only)
  Programmable one-shot timer
  Programmable periodic timer
  User-enabled stalling when the controller asserts CPU Halt flag during debug
  ADC event trigger
16-bit Input Capture modes
  Input edge count capture
  Input edge time capture
16-bit PWM mode
  Simple PWM mode with software-programmable output inversion of the PWM signal

## Slide 8: GPTM Module Block Diagram
GPTM

## Slide 9: Functional Description I
Overview
  Access of the features takes place through the StellarisWare® API
  The timer Application Programming Interface (API) provides a set of functions for dealing with the timer module
  Functions are provided to configure and control the timer, along with functions to modify timer/counter values, and to manage interrupt handling for the timer.
  The StellarisWare® driver is contained in driverlib/timer.c, with driverlib/timer.h containing the API definitions for use by applications
Link: see Chapter 3.4 “Stellarisware®” for further information.

## Slide 10: Functional Description II
Timer operating modes
  The timer module provides two 16-bit timer/counters that can be configured to operate independently as timers or event counters, or they can be configured to operate as one 32-bit timer or one 32-bit Real Time Clock (RTC)
  When configured as either a 32-bit or 16-bit timer, a timer can be set up to run as a one-shot timer or a continuous timer
  If configured as a one-shot timer, when it reaches zero the timer will cease counting
  If configured as a continuous timer, when it reaches zero the timer will continue counting from a reloaded value

## Slide 11: Functional Description III
Additional operating modes
  When configured as a 32-bit timer, the timer can also be configured to operate as an RTC.
  In that case, the timer expects to be driven by a 32.768 KHz external clock, which is divided down to produce 1 second clock ticks
  When in 16-bit mode, the timer can also be configured for event capture or as a Pulse Width Modulation (PWM) generator
  When configured for event capture, the timer acts as a counter. It can be configured to either count the time between events, or it can count the events themselves
  When a timer is configured as a PWM generator, the input line used to capture events becomes an output line, and the timer is used to drive an edge-aligned pulse onto that line

## Slide 12: Functional Description IV
Interrupts and Events
  Control is also provided over interrupt sources and events
  Interrupts can be generated to indicate that an event has been captured, or that a certain number of events have been captured
  Interrupts can also be generated when the timer has counted down to zero, or when the RTC matches a certain value

## Slide 13: Timer driver lib
The timer API consists of three function groups:
  Configuration and control
  Contents
  Interrupt-handling
Timer configuration
  Is handled by the function TimerConfigure()
  It is used to set up 32- or 16-bit modes, and
  To select between PWM, capture, and timer operations
Timer control
  Timer status is configured by a set of control functions:
  TimerEnable(), TimerDisable(), TimerControlLevel(), TimerControlTrigger(), TimerControlEvent(), TimerControlStall(), TimerRTCEnable(), and TimerRTCDisable()

## Slide 14: Timer driver lib II
Timer contents
  values and scaling of timers can be configured by the following set of functions:
  TimerLoadSet(), TimerLoadGet(), TimerPrescaleSet(), TimerPrescaleGet(), TimerMatchSet(), TimerMatchGet(), TimerPrescaleMatchSet(), TimerPrescaleMatchGet(), and TimerValueGet()
Timer Interrupts
  The interrupt handler for the Timer interrupt is managed by: TimerIntRegister() and TimerIntUnregister()
The individual interrupt sources within the timer module are managed by:
  TimerIntEnable(), TimerIntDisable(), TimerIntStatus(), and TimerIntClear()

## Slide 15: Example “Timers_blinky”
Description
  This example application demonstrates the use of the timers to generate periodic interrupts.
  One timer is set up to interrupt once per second and the other to interrupt twice per second.
  Each interrupt handler will toggle its own indicator on the display.
  Additionally the on-board LED is toggled by Timer0 ISR.
Learning elements
  Microcontroller
    GPIO (LED), Timer
  Evaluation Board
    On-board LED, On-board display
Functional test (debugging)
  Blinking on-Board LED
  Interrupt status on display
Link: see Lab “lab43a.zip”

## Slide 16: Example “Timers_blinky” Part I
#include "inc/hw_ints.h"
#include "inc/hw_memmap.h"
#include "inc/hw_types.h"
#include "driverlib/debug.h"
#include "driverlib/gpio.h"
#include "driverlib/interrupt.h"
#include "driverlib/sysctl.h"
#include "driverlib/timer.h"
#include "drivers/rit128x96x4.h"
#include "inc/lm3s1968.h" // HHN
unsigned long g_ulFlags;
//
// HHN
//
int g_LEDON;
...
Header files: GPIO, timers, display
Extension: HHN MEE-Project-Lab, SS11
Indicates status of LED

## Slide 17: Example “Timers_blinky” Part II
...
#ifdef DEBUG
void
__error__(char *pcFilename, unsigned long ulLine)
{
}
#endif
void
Timer0IntHandler(void)
{
//
// Clear the timer interrupt.
//
TimerIntClear(TIMER0_BASE, TIMER_TIMA_TIMEOUT);
//
// Toggle the flag for the first timer.
//
HWREGBITW(&g_ulFlags, 0) ^= 1;
...
Timer0 Interrupt Service Routine

## Slide 18: Example “Timers_blinky” Part III
...
//*****************************************************************************
//
// HHN
//
//*****************************************************************************
if (g_LEDON == 0)
{
//
// Turn on the LED.
//
GPIO_PORTG_DATA_R |= 0x04;
g_LEDON = 1;
}
else
{
//
// Turn off the LED.
//
GPIO_PORTG_DATA_R &= ~(0x04);
g_LEDON = 0;
}
//*****************************************************************************
...
Toggle LED on/off
Update g_LEDON variable

## Slide 19: Example “Timers_blinky” Part IV
...
//
// Update the interrupt status on the display.
//
IntMasterDisable();
RIT128x96x4StringDraw(HWREGBITW(&g_ulFlags, 0) ? "1" : "0", 48, 32, 15);
IntMasterEnable();
}
void
Timer1IntHandler(void)
{
//
// Clear the timer interrupt.
//
TimerIntClear(TIMER1_BASE, TIMER_TIMA_TIMEOUT);
//
// Toggle the flag for the second timer.
//
HWREGBITW(&g_ulFlags, 1) ^= 1;
...
Print information on the display
Timer1 Interrupt Service Routine

## Slide 20: Example “Timers_blinky” Part V
...
//
// Update the interrupt status on the display.
//
IntMasterDisable();
RIT128x96x4StringDraw(HWREGBITW(&g_ulFlags, 1) ? "1" : "0", 90, 32, 15);
IntMasterEnable();
}
int
main(void)
{
volatile unsigned long ulLoop; // HHN
//
// Set the clocking to run directly from the crystal.
//
SysCtlClockSet(SYSCTL_SYSDIV_1 | SYSCTL_USE_OSC | SYSCTL_OSC_MAIN |
SYSCTL_XTAL_8MHZ);
...
Print information on the Display
Main Routine

## Slide 21: Example “Timers_blinky” Part VI
...
//*****************************************************************************
//
//HHN
//
//*****************************************************************************
//
// Enable the GPIO port that is used for the on-board LED.
//
SYSCTL_RCGC2_R = SYSCTL_RCGC2_GPIOG;
//
// Do a dummy read to insert a few cycles after enabling the peripheral.
//
ulLoop = SYSCTL_RCGC2_R;
g_LEDON = 0; // PROLAB
//
// Enable the GPIO pin for the LED (PG2). Set the direction as output, and
// enable the GPIO pin for digital function.
//
GPIO_PORTG_DIR_R = 0x04;
GPIO_PORTG_DEN_R = 0x04;
...
Configure onboard LED

## Slide 22: Example “Timers_blinky” Part VII
...
//
// Initialize the OLED display and write status.
//
RIT128x96x4Init(1000000);
RIT128x96x4StringDraw("Timers example", 18, 24, 15);
RIT128x96x4StringDraw("T1: 0 T2: 0", 24, 32, 15);
//
// Enable the peripherals used by this example.
//
SysCtlPeripheralEnable(SYSCTL_PERIPH_TIMER0);
SysCtlPeripheralEnable(SYSCTL_PERIPH_TIMER1);
//
// Enable processor interrupts.
//
IntMasterEnable();
...
Configure OLED display
Enable interrupts

## Slide 23: Example “Timers_blinky” Part VIII
...
//
// Configure the two 32-bit periodic timers.
//
TimerConfigure(TIMER0_BASE, TIMER_CFG_32_BIT_PER);
TimerConfigure(TIMER1_BASE, TIMER_CFG_32_BIT_PER);
TimerLoadSet(TIMER0_BASE, TIMER_A, SysCtlClockGet());
TimerLoadSet(TIMER1_BASE, TIMER_A, SysCtlClockGet() / 2);
//
// Setup the interrupts for the timer timeouts.
//
IntEnable(INT_TIMER0A);
IntEnable(INT_TIMER1A);
TimerIntEnable(TIMER0_BASE, TIMER_TIMA_TIMEOUT);
TimerIntEnable(TIMER1_BASE, TIMER_TIMA_TIMEOUT);
//
// Enable the timers.
//
TimerEnable(TIMER0_BASE, TIMER_A);
TimerEnable(TIMER1_BASE, TIMER_A);
...
Configure timers
Enable timer interrupts
Enable timers

## Slide 24: Example “Timers_blinky” Part IX
...
//
// Loop forever while the timers run.
//
while(1)
{
}
}
Loop forever

## Slide 25: Questions and Exercises
Design a structured flowchart for “Timers_Blinky”.
Which programming model applies to “Timers_Blinky”?
What is PWM? Give an application example?
Exercise
  Modify the LED blink frequency.
  Implement a digital watch.

## Slide 26: Summary and Outlook
Summary
  From General-Purpose Timer Module to StellarisWare® API
  From “Blinky with loop” to “Blinky with timer”
Outlook/How to go on?
  The General-Purpose Timer Modules are basic functionality applied in the next labs

## Slide 27: References
[1] Texas Instruments: Data Sheet - Stellaris® LM3S1968. Chapter 9; spms037f.pdf, 2011.
[2] Texas Instruments: User’s Guide - Stellaris® LM3S1968 Evaluation Board. spmu037a.pdf, 2010.
[3] Texas Instruments: StellarisWare®. Path: \boards\ek-lm3s1968\ timers, 2011.
  [4] Brenner, S.; Mitsch, F.: Project Teaching ROM. Lab “Blinky with timer interrupts”; MEE-Project-Lab; HS Heilbronn, Campus KÜN, 20.06.2011.