## Slide 1: Chapter 2: Stellaris® family of microcontrollers
Stellaris® CortexTM-M3 - Microcontroller Family
Texas Instruments
Texas Instruments - University Program
Heilbronn University, Campus Künzelsau
Prof. Dr.-Ing. Ralf Gessler Rev. 1.0

## Slide 2: Content
Chapter 2: Stellaris® family of microcontrollers 2.1 Overview MCU 2.2 CortexTM -M3: Processor and Peripherals 2.3 CortexTM -M3: Programmer model (ISA) 2.4 Peripherals
Topics: MCU, ARM® processor core, on-chip memory, system peripherals, serial interface peripherals, motion control peripherals, analog peripherals

## Slide 3: Learning Objectives
The chapter describes the basics (theory) of the Stellaris® Family
  Architecture (common)
  Stellaris® Module “System”.
Additional Links for the other Stellaris® Modules are given.
Structure and questions:
  What are the features of the Stellaris® family?
  What are the Stellaris® product lines?
  What does a Stellaris® Module “System” looks like?

## Slide 4: Overview MCU
Microcontroller Unit (MCU)
ARM® CortexTM -M3 Processor Core
  Up to 100 MHz
  Joint Test Action Group (JTAG) Interface
  Nested Vectored Interrupt Ctrl. (NVIC)
  Serial Wire Debug (SWD)
On-chip Memory
  256 KB Flash, 96 KB SRAM
  ROM loaded with Stellaris® DriverLib,
  Bootloader, AES tables, and CRC
System Peripherals
  32-channel DMA Controller
  Internal Precision 16MHz Oscillator
  Two watchdog timers with separate clock domains
  ARM Cortex SysTick Timer
  4x 32-bit timers (up to 8 16-bit) with RTC capability
80 MHz

## Slide 5: Overview (cont.)
System Peripherals (cont.)
  Lower-power battery-backed hibernation module
  External Peripheral Interface (EPI)
    32-bit dedicated parallel bus for external peripherals
    Supports SDRAM, SRAM/Flash, M2M
Serial Interface Peripherals
  3 Univ. Asyn. Rec./Trans. (UARTs) with Infrared Data Association (IrDA) and ISO 7816 support
  2 Synchronous Serial Interfaces (SSI)
  10/100 Ethernet MAC and PHY
  Universal Serial Bus (USB) (full speed) OTG / Host / Device
  3 Controller Area Network (CAN) 2.0 A/B Controllers
  2 Inter-Integrated Circuits (I2Cs)
  Integrated Interchip Sound (I2S)
80 MHz

## Slide 6: Overview (cont.)
Motion Control Peripherals
  8 advanced PWM outputs for motion and energy applications
  2 Quadrature Encoder Inputs (QEI)
Analog Peripherals
  2 x 8-ch 10-bit ADC (for a total of 16 channels)
  3 analog comparators
  On-chip voltage regulator (1.2V internal operation)
  Low-Drop-Out (LDO)
Flexible pin-muxing capability
80 MHz

## Slide 7: Device Choice
Product lines: LM3S1nnn to LM3S9nnn
ARM® CortexTM-M3 Processor Core
  Same CortexTM -M3 core
  CPU frequency depends on product lines
Memory
  Size of internal Flash and SRAM depends on product lines
System peripherals
  Quantity depends on product lines
same
functionality

## Slide 8: Device Choice (cont.)
Serial interface peripherals
  Features depends on product lines
Motion control peripherals
  Features depends on product lines
Analog peripherals
  Features depends on product lines
Note: For each target application a product line
functionality
depends on
product line

## Slide 9: Section Links: Peripherals
ARM® CortexTM -M3 Processor Core
  More Details see: Chapter 2.3 “Cortex® -M3: Programmer model (ISA)”
On-Chip Memory
  More Details see: Chapter 2.2 “Cortex® -M3: Processor and Peripherals”
Serial Interfaces Peripherals
  More Details see: Module 2.4 “Peripherals”: UART, SSI, I2C - LM3S1968 Module 5.3 “Connectivity”: Ethernet, USB - LM3S9B92
Motion Control Peripherals
  More Details see: Chapter 2.4 “Peripherals” - LM3S1968
Analog Peripherals
  More Details see: Chapter 2.4 “Peripherals” - LM3S1968

## Slide 10: System Peripherals
80 MHz

## Slide 11: Clock architecture
Main OSCillator (OSC)
  3.579545 MHz through 16.384 MHz if PLL used
Precision Internal Oscillator (PIOSC)
  On-chip precision 16 MHz clock (clk) (±1% at room temperature)
  Does not require any external components
Internal OSC
Hibernation OSC

## Slide 12: Example: System Control
System Control determines the overall operation of the device. It controls the clocking of the device, the set of peripherals that are enabled, configuration of the device, its resets and provides information about the device.
System Control is part of Stellaris® Peripheral Driver Library.
  Link: see Chapter 3.4 “StellarisWare®”
Example:
  Link: see Lab “lab21a.zip”
…
//
// Set the clocking to run directly from the crystal.
//
SysCtlClockSet(SYSCTL_SYSDIV_1 | SYSCTL_USE_OSC | SYSCTL_OSC_MAIN |
SYSCTL_XTAL_8MHZ);
…

## Slide 13: Reset
Flexible Reset Sources
  Power-on Reset (POR)
  Reset pin assertion
  Brown-Out Reset (BOR) detector alerts to system power drops
    The system provides a brown-out detection circuit that triggers if the power supply (VDD) drops below a Voltage Brown-out THreshold (VBTH). If a brown-out condition is detected, the system may generate a controller interrupt or a system reset.
    This is initially disabled and may be enabled by software.
  Software reset
  Watchdog timer reset

## Slide 14: System Control
For power-savings purposes, the RCGCn , SCGCn , and DCGCn registers control the clock gating logic for each peripheral or block in the system while the controller is in Run, Sleep, and Deep-Sleep mode, respectively.
There are four levels of operation for the device defined as:
  Run Mode: the controller actively executes code
  Sleep Mode: the clock frequency of the active peripherals is unchanged, but the processor and the memory subsystem are not clocked and therefore no longer execute code. Sleep mode is entered by the Cortex-M3 core executing a WFI (Wait for Interrupt) instruction. Any properly configured interrupt event in the system will bring the processor back into Run mode.

## Slide 15: System Control (cont.)
There are four levels of operation for the device defined as (cont.):
  Deep-Sleep Mode: the clock frequency of the active peripherals may change (depending on the Run mode clock configuration) in addition to the processor clock being stopped. An interrupt returns the device to Run mode from one of the sleep modes.
  Hibernate Mode: the power supplies are turned off to the main part of the device and only the Hibernation module's circuitry is active. An external wake event or Real Time Clock (RTC) event is required to bring the device back to Run mode.

## Slide 16: System Timer
CortexTM -M3 includes an integrated system timer, SysTick. SysTick provides a simple, 24-bit clear-on-write, decrementing, wrap-on-zero counter with a flexible control mechanism.
Link: see Chapter 2.2 “CortexTM -M3: Processor and Peripherals”

## Slide 17: Timers
Up to 4 timer modules
  Each configurable as single 32-bit timer, or two 16-bit timers
32-bit Timer Modes
  32-bit programmable one-shot timer with selectable clock
  32-bit programmable periodic timer with selectable clock
  RTC using a 32.768 kHz input clock
  Software controlled debug event stalling (except for the RTC function)
16-bit Timer Modes
  16-bit general-purpose timer with 8-bit pre-scaler and input clock selection
  General-purpose free running timer modes: one-shot or periodic
  Selectable debug event stalling
16-bit Capture Modes (CCP)
  Input edge count capture
  Input edge time capture
PWM mode
  Simple PWM mode with programmable output negation

## Slide 18: Timers: PWM
PWM signals are driven through CCPx output

## Slide 19: Watchdog Timers
Allows software to regain control when there is a system failure caused by software error or an external device
Generates an interrupt or system reset on time-out
Configuration can be locked (key) to prevent inadvertent changes
User-enabled stalling for software debugging
Some Stellaris® MCUs feature two Watchdog Timer Modules, where :
  One module is clocked by the system clock (Watchdog Timer 0)
  One module is clocked by the PIOSC (Watchdog Timer 1).

## Slide 20: Example: Watchdog Timer
Watchdog Timer is part of Stellaris® Peripheral Driver Library.
The Watchdog Timer Application Programming Interface (API) provides a set of functions for using the Stellaris® watchdog timer modules. Functions are provided to deal with the watchdog timer interrupts, and to handle status and configuration of the watchdog timer.
Link Chapter 3.4 “StellarisWare®”
The following example shows how to set up the watchdog timer API. If the watchdog is not periodically fed, it will reset the system. Each time the watchdog is fed, the LED is inverted so that it is easy to see that it is being fed, which occurs once every second.
Link see Lab “lab21a.zip”
  Note: example, not a complete application!

## Slide 21: Example: Watchdog Timer (cont.)
…
//
// Enable the watchdog interrupt.
//
IntEnable(INT_WATCHDOG);
//
// Set the period of the watchdog timer.
//
WatchdogReloadSet(WATCHDOG0_BASE, SysCtlClockGet());
//
// Enable reset generation from the watchdog timer.
//
WatchdogResetEnable(WATCHDOG0_BASE);
//
// Enable the watchdog timer.
//
WatchdogEnable(WATCHDOG0_BASE);
//
// Loop forever while the LED winks as watchdog interrupts are handled.
//
while(1)
{
}
…

## Slide 22: GPIOs
General Purpose Input/Outputs (GPIOs)
Programmable pad configuration through GPIO module
Any GPIO can be full featured external interrupt
Bit addressable pins, atomic operation
Fast output toggling: Toggle rate up to ½ the CPU clock
5-V-tolerant inputs

## Slide 23: GPIOs (cont.)
Up to 61 GPIO available on a single device
Programmable Drive Strength
  2 mA, 4 mA, 8 mA or 8 mA with slew rate control
Programmable weak pull-up, pull-down
Open drain enables
Digital input enables
Link: see Chapter 4.1 “General Purpose Input/Output (GPIO)”

## Slide 24: Direct Memory Access
Direct Memory Access (DMA)
32-channel configurable μDMA controller
Dedicated channels for supported peripherals
  One channel each for receive and transmit path for bidirectional peripherals
  Multiple data sizes, Two levels of priority, Maskable device requests
Interrupt on transfer completion with a separate interrupt per channel
Support for multiple transfer modes:
  Basic, for simple transfer scenarios
  Ping-pong, for continuous data flow to/from peripherals
  Scatter-gather, from a programmable list of arbitrary transfers initiated from a single request
DMA requests
  UART, Timer, USB, Ethernet, ADC, SSI, External Peripherals I/F

## Slide 25: DMA (cont.)

## Slide 26: External Peripheral Interface
External Peripheral Interface (EPI)
Multiple device types supported
  SDRAM: Supports x16 (Single Data Rate) at up to 50MHz
    Supports low-cost SDRAMS up to 64 MB
    Includes automatic refresh and access to all banks/rows
    Includes a sleep/standby mode to keep contents alive with minimal power draw
  Host-Bus Interface: Traditional x8 and x16 MCU bus interface capabilities
    Support of both muxed and de-muxed address and data
    Access to SRAM, NOR Flash, and other devices, with up to 1MB of addressing or up to 256 MB for muxed mode
    Speed controlled, with read and write data wait-state counters
  Machine-to-Machine (M2M): Wide parallel interfaces for fast communications
    For instance, CPLDs and FPGAs
    Data widths up to 32-bits, data rates up to 150 Mbytes/second
    Optional “address” sizes from 4-bits to 16-bits
    Optional clk output, read/write strobes, framing (with counter-based size), and clk-enable input
Other features
  General parallel GPIO, FIFOed with speed control
  Blocking and non-blocking reads
  FIFOed writes separate the processor from timing details
  Direct memory access (DMA)

## Slide 27: EPI block diagram
External Peripheral Interface (EPI)
Cortex M3
Stellaris
DMA

## Slide 28: Hibernation module
Two mechanisms for power control
  System power control using discrete external regulator
  On-chip power control using internal switches under register control
Dedicated pin for waking using an external signal
Low-battery detection, signaling, and interrupt generation
32-bit real-time counter (RTC)
  Two 32-bit RTC match registers for timed wake-up and interrupt generation
  RTC pre-divider trim for making fine adjustments to the clock rate
Clock source from a 32.768 kHz external oscillator or a 4.194304 MHz crystal - 32.768 kHz external oscillator can be used for main clock
64 32-bit words of non-volatile memory to save state during hibernation
Programmable interrupts for RTC match, external wake, and low battery events

## Slide 29: Power architecture
3 power domains
  Core Supply: VDDC
  Supply Voltage: VDD
  Analog circuitry: VDDA

## Slide 30: Power consumption
Battery-backed Hibernation Module (Standby current as low as 10μA)
  32-bit real-time counter (RTC)
    Programmable 32.768 kHz external oscillator or a 4.194304 MHz crystal
    RTC software trim for making fine adjustments to the clock rate
  Power-switching logic to discrete external regulator (switch to battery)
  Low-battery detection, signaling, and interrupt generation
  Wake on RTC match and / or external pin
On-chip Low Drop-Out (LDO) voltage regulator
Low-power options on controller: Sleep and Deep-sleep modes
Low-power options for peripherals: software controls shutdown of individual peripherals
3.3V supply brown-out detection and reporting via interrupt or reset

## Slide 31: Power consumption (cont.)
Note: Battery supply current (Ibat)
 | SRAM saved | Lowest Ibat | Lowest type wake-up
Running mode | Yes | 1.12 mA/MHz | N/A
Sleep mode | Yes | 8 mA | 0.427μs
Deep-Sleep mode | Yes | 550 μA | 0.427μs
Hibernate RTC ON | 256 bytes saved | 18 μA | 62 μs
Hibernate RTC OFF | 256 bytes saved | 8 μA | 10 ms

## Slide 32: Example: Sleep Mode
SysCtlSleep and SysTick are parts of System Control (Stellaris® Peripheral Driver Library).
CPUUsage is part of LM3S1968 Firmware Development Package.
Link: see Chapter 3.4 “StellarisWare®”
Link: see Lab “lab21b.zip”
  Note: example, not a complete application!
The following example shows how to use the CPU usage module to measure the CPU usage where the foreground simply burns some cycles.

## Slide 33: Example: Sleep Mode
…
//
// The CPU usage for the most recent time period.
//
unsigned long g_ulCPUUsage;
//
// Handles the SysTick interrupt.
//
void
SysTickIntHandler(void)
{
//
// Compute the CPU usage for the last time period.
//
g_ulCPUUsage = CPUUsageTick();
}
//
// The main application.
//
int
main(void)
{
//
// Initialize the CPU usage module, using timer 0.
//
CPUUsageInit(8000000, 100, 0);
…
…
//
// Initialize SysTick to interrupt at 100 Hz.
//
SysTickPeriodSet(8000000 / 100);
SysTickIntEnable();
SysTickEnable();
//
// Loop forever.
//
while(1)
{
//
// Delay for a little bit so that CPU usage is not zero.
//
SysCtlDelay(100);
//
// Put the processor to sleep.
//
SysCtlSleep();
}
}
…

## Slide 34: Questions and Exercises
What are the main modules of the Stellaris® family?
Explain a Watchdog Timer.
Explain Hibernation.
What is DMA?

## Slide 35: Summary and Outlook
Summary
  From the Stellaris® Family Architecture in common to Stellaris® family product lines
  From the Device Choice to Module “System”
Outlook/How to go on?
  Chapter 4: “Peripheral Programming in C” shows the practical use in C

## Slide 36: References
[1] Henri, G.; Texas Instruments: MCU Training Module - System and Peripherals. EMEA, Oct. 7, 2010.
[2] Henri, G.; Texas Instruments: MCU Training Module - Solution overview. EMEA, Jul. 21, 2010.
[3] Texas Instruments: Data Sheet - Stellaris® LM3S1968. Chapter 1: “Architectural Overview”, Chapter 5.1.5: “System Control”, spms037f.pdf, 2011.
[4] Texas Instruments: User’s Guide - Stellaris Peripheral Driver Library. SW-DRL-UG-6075.pdf, 2010.
[5] Texas Instruments: User’s Guide - EK-LM3S1968 Firmware Development Package. SW-EK-LM3S1968-UG-6075.pdf, 2010.